## Slide 1: Analysis of Branch Predictor Choices and their Impact on Performance of 8086 Microprocessor using Gem5 Simulator
Team Members:
Rubina Parveen (RXL220014)
Neha Gangalapudi (NXG220043)
Allocate Marks ( 100/100)

## Slide 2: Initial Set-Up
For this Project we have used Gem5 installed on the UTD Server.
Copied the Gem5 to our Local Directory using the command: “cp –rf /usr/local/gem5/home/010/r/rx/rxl220014/CA/gem5
Compiled using the command: “scons build/X86/gem5.opt”.
After Compiling, we cloned the Benchmark Files to our local directory using the command provided: “git clone https://github.com/timberjack/Project1_SPEC.git”.

## Slide 3: Branch Predictor
A branch predictor is a crucial component of a pipelined CPU that helps improve its performance.
It works by attempting to anticipate the address of a branch instruction well in advance and with limited context, organizing the most likely outcome.
Despite having access to only the current instruction's address and a limited history, the predictor operates before the decoder pipeline phase.

## Slide 4: Types of Predictors Used
Tournament Predictor: It improves the accuracy of predictions by using a combination of two or more other branch predictors.
  Uses a meta-predictor to determine which of the branch predictors should be used for each branch instruction. The meta-predictor compares the accuracy of the predictions made by the different predictors and selects the one with the highest accuracy for each branch.
  This approach can provide higher prediction accuracy than any individual predictor alone.

## Slide 5
Local Predictor: Makes a prediction depending on the outcome of a branch for its last ten executions.
  Stores a table of the history of branches at each location and uses this information to make predictions.
  Local predictors work well when a program has repeating patterns of branches at specific locations.

## Slide 6
Bi-mode Predictor: It is a hybrid of local and global predictor. The bi-mode predictor uses a local predictor to predict the outcome of branches at specific locations in the program and a global predictor to predict branches that do not have a history at the current location.
  The global predictor uses a history buffer to store the history of recent branches in the program and uses this information to make predictions.
  The bi-mode predictor selects either the local or global predictor based on the history of recent branches at the current location in the program.

## Slide 7: Project Requirements and Specifications
Objective
  To Simulate different branch predictors over different benchmarks and observing their behavior hierarchy in X86 architecture on Gem5 simulator .
Tools Used
  Gem5 simulator on the university server
  MobaXterm: For remote SSH extension to access Gem5 over university server
  Benchmarks: (1)401.bzip2 (2) 429.mcf (3) 456.hmmer (4) 458.sjeng (5) 470.lbm
  Branch Predictors: (1) LocalBP( ) (2) TournamentBP ( ) (3) BiModeBP( )
  Shell Script: Created a shell script project2.sh for the project

## Slide 8: Deliverables
  Changes made to source files.
  Observing the changes made.
  Generating the BTBMissPct and BranchMispredPercent for all Benchmarks
  Varying the sizes of predictor and calculating the same for TournamentBP
  Graphs of each benchamark for each Branch Predictor
  Observations from the graphs.

## Slide 9: Changes in Gem5
We made the following changes to the respective “runGem5.sh” files for the Benchmarks 401.bzip2, 429.mcf, 456.hmmer, 458.sjeng and 470.lbm
Change the Argument path in every benchmark
Change the path of the gem5 directory

## Slide 10
In the Gem5 folder, to change the branch predictor type
Go to cd gem5/src/cpu/simple .
Edit the file named “BaseSimpleCPU.py” and at the bottom we find the line: branchPred = Param.BranchPredictor (NULL, “Branch Predictor”)
In place of null we put the branch predictor types given: 1. LocalBP 2. BimodeBP 3. TournamentBP.
After changing each BP, delete all the files gem5/build/X86 first and then use the scons (% scons build/X86/gem5.opt) command to recompile in order to reflect the changes.

## Slide 11: Changes to source files
Changes in bpred_unit.cc file for adding the definition of BTBMissPct
Changes in base.cc file for definition of BranchMispredPercent
Changes in exec_context.hh file

## Slide 12
We make following changes in sizes of the predictor in gem5 in file: gem5/src/cpu/pred/Branchpredictor.py
In class BranchPredictor : Number of BTB entries is changed .
In class LocalBP: Size of local predictor is changed

## Slide 13
In class TournamentBP: localPredictorSize, globalPredictorSize and choicePredictorSize are changed
In class BiModeBP: globalPredictorSize and choicePredictorSize are changed

## Slide 14
Outputs to be observed after compiling
After making the necessary changes we run the script for all the benchmarks, for all the three Branch Predictors separately and compare the results for different Branch Predictors.
Then in m5out/config.ini file of every benchmark, we observe if the type of system.cpu.pred is the same as the predictor we have changed.

## Slide 15
We can find the results in our m5out/stats.txt file of every benchmark

## Slide 16
We made a file branchpred.txt where all the outputs that we need are captured and stored of all benchmarks in a single file.

## Slide 17: BTB Miss Pct of all Benchmarks for all types of Predictor
Chart: Graph for BTB Miss Percentage
| 401.bzip2 | 429.mcf | 456.hmmer | 458.sjeng | 470.lbm
BTBMissPct for Local BP | 0.18055 | 8.5223 | 2.4912 | 9.3013 | 22.4904
BTBMissPct for Tournament BP | 0.1371 | 4.6382 | 1.7684 | 4.7763 | 46.4655
BTBMissPct for Bi-Mode BP | 0.13596 | 2.5026 | 0.67068 | 7.1026 | 0.14566

## Slide 18
Chart: BTB Miss Percentage for Benchmark 401.bzip2
| for Local BP | for Tournament BP | for Bi-Mode BP
401.bzip2 | 0.18055 | 0.1371 | 0.13596
Chart: BTB Miss Percentage for Benchmark 429.mcf
| for Local BP | for Tournament BP | for Bi-Mode BP
429.mcf | 8.5223 | 4.6382 | 2.5026
Chart: BTB Miss Percentage for Benchmark 456.hmmer
| for Local BP | for Tournament BP | for Bi-Mode BP
456.hmmer | 2.4912 | 1.7684 | 0.67068

## Slide 19
Chart: BTB Miss Percentage for Benchmark 458.sjeng
| for Local BP | for Tournament BP | for Bi-Mode BP
458.sjeng | 9.3013 | 4.7763 | 7.1026
Chart: BTB Miss Percentage for Benchmark 470.lbm
| for Local BP | for Tournament BP | for Bi-Mode BP
470.lbm | 22.4904 | 46.4655 | 0.14566

## Slide 20: Branch MispredPercent of all benchmarks for all types of predictors.
Chart: Graph for Percentage of Branch Misprediction
| 401.bzip2 | 429.mcf | 456.hmmer | 458.sjeng | 470.lbm
BTBMissPredPercent for Local BP | 6.423 | 10.2013 | 14.4059 | 14.3861 | 0.595
BTBMissPredPercent for Tournament BP | 5.9576 | 4.9711 | 9.4821 | 9.7943 | 0.64798
BTBMissPredPercent for Bi-Mode BP | 5.8611 | 5.6373 | 10.5931 | 10.2173 | 0.81163

## Slide 21
Chart: Percentage of BranchMissPrediction for Benchmark 401.bzip2
| for Local BP | for Tournament BP | for Bi-Mode BP
401.bzip2 | 6.423 | 5.9576 | 5.8611
Chart: Percentage of BranchMissPrediction for Benchmark 429.mcf
| for Local BP | for Tournament BP | for Bi-Mode BP
429.mcf | 10.2013 | 4.9711 | 5.6373
Chart: Percentage of BranchMissPrediction for Benchmark 456.hmmer
| for Local BP | for Tournament BP | for Bi-Mode BP
456.hmmer | 14.4059 | 9.4821 | 10.5931

## Slide 22
Chart: Percentage of BranchMissPrediction for Benchmark 458.sjeng
| for Local BP | for Tournament BP | for Bi-Mode BP
458.sjeng | 14.3861 | 9.7943 | 10.2173
Chart: Percentage of BranchMissPrediction for Benchmark 470.lbm
| for Local BP | for Tournament BP | for Bi-Mode BP
470.lbm | 0.595 | 0.64798 | 0.81163

## Slide 23: Observations & Conclusion
From the graphs obtained we can say that for the given combination of branch predictor sizes the BiMode BP is giving the least BTB miss percentage for benchmarks 401.bzip2, 429.mcf, 456.hmmer and 470.lbm and Tournament BP is giving least BTB miss percentage for 458.sjeng.
  The best result we obtained for benchmark 401.bzip2 : Branch Predictor-BiMode BP, BTB miss percent = 0.135964, BTB Entry = 2048 and Predictor size = 2048.
The Tournament BP is giving the least branch miss prediction percentage for 429.mcf, 456.hmmer, 458.sjeng, for 401.bzip2 it is BiMode BP and for 470.lbm it is Local BP.
  The best result we obtained for benchmark 470.lbm : Branch Predictor-Local BP, Branch miss percent = 0.595001, BTB Entry = 2048 and Predictor size: Local=1024, Global=4096, Choice = 4096.

## Slide 24
Therefore, for the benchmark 401.bzip2 the best performance is achieved by BiMode BP with a BTB miss percentage of 0.135964 and a Branch miss percentage of 5.861087
For benchmark 429.mcf, we can choose BiMode BP as it is giving the least BTB miss percentage of 2.502616 and a Branch miss percentage of 5.637336.
We can choose BiMode BP for benchmark 456.hmmer as it is providing the best tradeoff between the BTB miss percentage and Branch Miss percentage when compared to Tournament BP. The BTB miss percentage by BiMode is 0.670678 and the Branch Miss Prediction percent is 9.482139.
For benchmark 458.sjeng the Tournament BP gives the best results with a BTB miss percentage of 4.776297 and Branch Prediction miss percentage of 9.794284.
Lastly for Benchmark 470.lbm, the best performance is with Local BP for the Branch Prediction Miss percentage, but it gives more BTB misses when compared to BiMode BP.
The BiMode BP outperforms the other two Branch Predictors for most of the benchmarks for the given specifications.

## Slide 25: BTB MissPct values for all Benchmarks for Tournament Branch Predictor

## Slide 26
Keeping the BTBentries value same and changing the sizes of Local Predictor (LP), Global Predictor(GP), Choice Predictor (CP) and observing the changes in BTB Miss percentage for all benchmarks using graphs.
Chart: BTB Miss Percentage for Benchmark 401.bzip2
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
401.bzip2 | 0.13884 | 0.13375 | 0.19267 | 0.1371 | 0.1394 | 0.13717 | 0.14725 | 0.14575 | 0.12902 | 0.13626 | 0.13665 | 0.11632 | 0.13594 | 0.087591
Chart: BTB Miss Percentage for Benchmark 429.mcf
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
429.mcf | 4.9651 | 5.8987 | 3.9047 | 4.6382 | 8.8761 | 5.7883 | 7.2066 | 6.4875 | 5.6742 | 4.5997 | 5.2676 | 6.4842 | 5.1112 | 5.0389
As LP,GP & CP sizes increases, BTB MissPct decreases.
As LP,GP & CP sizes increases, BTB MissPct remains almost decreases.

## Slide 27
Chart: BTB Miss Percentage for Benchmark 456.hmmer
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
456.hmmer | 1.0642 | 1.0209 | 0.67056 | 1.7684 | 2.4545 | 1.1032 | 0.80914 | 0.75677 | 0.84179 | 2.026 | 0.35157 | 0.85036 | 0.9418 | 0.8796
Chart: BTB Miss Percentage for Benchmark 458.sjeng
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
458.sjeng | 4.858 | 4.9829 | 5.6323 | 4.7763 | 5.1844 | 5.1693 | 5.3557 | 4.841 | 4.9915 | 4.8215 | 5.0979 | 9.6715 | 4.7294 | 4.9121
As LP,GP & CP sizes increases, BTB MissPct decreases.
As LP,GP & CP sizes increases, BTB MissPct increases.

## Slide 28
Chart: BTB Miss Percentage for Benchmark 470.lbm
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
470.lbm | 46.4651 | 46.4655 | 46.4647 | 46.4655 | 6.2249 | 46.5279 | 6.7511 | 46.4653 | 46.4657 | 46.4657 | 46.5225 | 46.4707 | 46.4707 | 46.4698
As LP,GP & CP sizes increases, BTB MissPct increases.

## Slide 29
Chart: BTB MissPct values for varying predictor sizes in TornamentBP
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
BTB Miss Pct 401.bzip2 | 0.13884 | 0.13375 | 0.19267 | 0.1371 | 0.1394 | 0.13717 | 0.14725 | 0.14575 | 0.12902 | 0.13626 | 0.13665 | 0.11632 | 0.13594 | 0.087591
BTB Miss Pct 429.mcf | 4.9651 | 5.8987 | 3.9047 | 4.6382 | 8.8761 | 5.7883 | 7.2066 | 6.4875 | 5.6742 | 4.5997 | 5.2676 | 6.4842 | 5.1112 | 5.0389
BTB Miss Pct 456.hmmer | 1.0642 | 1.0209 | 0.67056 | 1.7684 | 2.4545 | 1.1032 | 0.80914 | 0.75677 | 0.84179 | 2.026 | 0.35157 | 0.85036 | 0.9418 | 0.8796
BTB Miss Pct 458.sjeng | 4.858 | 4.9829 | 5.6323 | 4.7763 | 5.1844 | 5.1693 | 5.3557 | 4.841 | 4.9915 | 4.8215 | 5.0979 | 9.6715 | 4.7294 | 4.9121
BTB Miss Pct 470.lbm | 46.4651 | 46.4655 | 46.4647 | 46.4655 | 6.2249 | 46.5279 | 6.7511 | 46.4653 | 46.4657 | 46.4657 | 46.5225 | 46.4707 | 46.4707 | 46.4698

## Slide 30: Branch Mispred Percentage for all Benchmarks for Tournament Branch Predictor

## Slide 31
Keeping the BTB value same and changing the sizes of Local Predictor (LP), Global Predictor (GP), Choice Predictor (CP) and observing the changes in Percentage of Branch Miss Prediction for all benchmarks using graphs.
Chart: Percentage of BranchMissPrediction for Benchmark 401.bzip2
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
401.bzip2 | 5.9985 | 5.9819 | 6.0069 | 5.9576 | 5.9904 | 5.9232 | 5.9849 | 5.9844 | 5.9693 | 5.9432 | 5.9113 | 5.9471 | 5.9236 | 5.9379
Chart: Percentage of BranchMissPrediction for Benchmark 429.mcf
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
429.mcf | 5.1462 | 5.0926 | 5.3045 | 4.9711 | 5.1069 | 4.8968 | 5.1092 | 5.0853 | 5.028 | 4.905 | 4.8331 | 4.9824 | 4.8688 | 4.9516
As LP,GP & CP size increases, Percentage of Branch Miss prediction decreases.
As LP, GP & CP size increases, Percentage of Branch Miss prediction decreases.

## Slide 32
Chart: Percentage of BranchMissPrediction for Benchmark 456.hmmer
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
456.hmmer | 9.9611 | 9.7848 | 10.348 | 9.4821 | 9.7084 | 9.2233 | 8.636 | 8.6355 | 8.5176 | 8.2215 | 8.0809 | 8.3832 | 8 | 8.2938
Chart: Percentage of BranchMissPrediction for Benchmark 458.sjeng
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
458.sjeng | 10.4533 | 10.2513 | 11.3058 | 9.7943 | 10.8726 | 9.8612 | 10.801 | 10.1317 | 9.9511 | 9.5436 | 9.653 | 9.6715 | 9.3037 | 9.4861
As LP, GP & CP size increases, Percentage of Branch Miss prediction decreases.
As LP, GP & CP size increases, Percentage of Branch Miss prediction decreases.

## Slide 33
Chart: Percentage of BranchMissPrediction for Benchmark 470.lbm
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
470.lbm | 0.64798 | 0.64796 | 0.64797 | 0.64798 | 0.35686 | 0.34996 | 0.35893 | 0.62951 | 0.62948 | 0.6295 | 0.35862 | 0.62271 | 0.62272 | 0.60467
As LP,GP & CP size increases, Percentage of Branch Miss prediction decreases.

## Slide 34
Chart: BTB MissPred Percent values for varying predictor sizes in TornamentBP
| 1024_2048_1024 | 1024_2048_2048 | 1024_4096_1024 | 1024_4096_4096 | 1024_8192_1024 | 1024_8192_8192 | 2048_1024_2048 | 2048_2048_1024 | 2048_2048_2048 | 2048_4096_4096 | 2048_8192_8192 | 4096_2048_2048 | 4096_4096_4096 | 8194_2048_2048
BTB MissPredPercent 401.bzip2 | 5.9985 | 5.9819 | 6.0069 | 5.9576 | 5.9904 | 5.9232 | 5.9849 | 5.9844 | 5.9693 | 5.9432 | 5.9113 | 5.9471 | 5.9236 | 5.9379
BTB MissPredPercent 429.mcf | 5.1462 | 5.0926 | 5.3045 | 4.9711 | 5.1069 | 4.8968 | 5.1092 | 5.0853 | 5.028 | 4.905 | 4.8331 | 4.9824 | 4.8688 | 4.9516
BTB MissPredPercent 456.hmmer | 9.9611 | 9.7848 | 10.348 | 9.4821 | 9.7084 | 9.2233 | 8.636 | 8.6355 | 8.5176 | 8.2215 | 8.0809 | 8.3832 | 8 | 8.2938
BTB MissPredPercent 458.sjeng | 10.4533 | 10.2513 | 11.3058 | 9.7943 | 10.8726 | 9.8612 | 10.801 | 10.1317 | 9.9511 | 9.5436 | 9.653 | 9.6715 | 9.3037 | 9.4861
BTB MissPredPercent 470.lbm | 0.64798 | 0.64796 | 0.64797 | 0.64798 | 0.35686 | 0.34996 | 0.35893 | 0.62951 | 0.62948 | 0.6295 | 0.35862 | 0.62271 | 0.62272 | 0.60467

## Slide 35: BTB Miss Percentage after changing the BTB entries

## Slide 36: Branch Prediction Miss Percentage after changing the BTB entries

## Slide 37: Observations & Conclusion
For the Tournament BP
  We observe that as the sizes of the 3 predictors increase the BTB Miss percentage decrease for benchmarks 401.bzip2, 429.mcf, 456.hmmer and increases for 458.sjeng and 470.lbm if we keep the BTB Entries constant. Branch prediction miss percentage decrease if we keep the BTB Entries constant for all the 5 benchmarks.
  If we change the BTB Entries and vary the 3 predictors sizes as well, we observe that as the BTB Entries size and the predictor sizes increase the BTB Miss percentage and the Branch Miss Prediction Percentage decreases.
  We are getting the least BTB miss percentage for benchmark 401.bzip2 if we change both the BTB entries and predictor sizes and the lease branch miss predictions for benchmark 470.lbm.
  But the Tournament BP can best perform for Benchmarks 401.bzip2 and 429.mcf, not for the other 3 benchmarks as it gives either BTB miss percentage too high, or the branch miss prediction percentage is too high.

## Slide 38
Thank You